BILCO Type FPG-Fall Protection Grating System allows workers to safely inspect pumps and monitor underground areas. Meeting OSHA 29 CFR 1926.502(c) requirements for fall protection on access doors, the system is available from BILCO as a factory installed option on selected models.  For more information, please visit our website www.bilco.com or call 1-800-854-9724.

SECTION 083100

FLOOR ACCESS DOORS

(BILCO TYPE FPG)

GENERAL

SUMMARY

Work Included:  Provide factory-fabricated floor access doors.

SUBMITTALS

Product Data:  Submit manufacturer’s product data.

Shop Drawings: Submit shop drawings including profiles, accessories, location, adjacent construction interface, and dimensions.

Warranty:  Submit executed copy of manufacturer’s standard warranty.

QUALITY ASSURANCE

Manufacturer:  A minimum of 5 years experience manufacturing similar products.

Installer:  A minimum of 2 years experience installing similar products.

Manufacturer’s Quality System: Registered to ISO 9001 Quality Standards including in-house engineering for product design activities.

DELIVERY, STORAGE AND HANDLING

Deliver products in manufacturer’s original packaging.  Store materials in a dry, protected, well-vented area. Inspect product upon receipt and report damaged material immediately to delivering carrier and note such damage on the carrier’s freight bill of lading.

WARRANTY

Manufacturer’s Warranty:  Provide manufacturer’s standard warranty.  Materials shall be free of defects in material and workmanship for a period of twenty-five years from the date of purchase. Should a part fail to function in normal use within this period, manufacturer shall furnish a new part at no charge.

PRODUCTS

MANUFACTURER

Basis-of-Design Manufacturer: Type FPG - Fall Protection Grating System by The BILCO Company, P.O. Box 1203, New Haven, CT 06505, 1-800-854-9724, Fax: 1-203-535-1582, Web: www.bilco.com.

FALL PROTECTION GRATING SYSTEM

Furnish and install on vault access doors, where indicated on plans, fall protection grating system.  Door manufacturer shall install the grating system when the door is fabricated or field install (by others) on existing doors already in use. If field installation is necessary, grating system shall be installed per the manufacturer’s instructions.

Performance characteristics:

Grating panel(s) shall be high visibility safety yellow in color.

Grating panel(s) shall lock automatically in the full open position.

Grating system shall have a twenty-five year warranty.

Grating panel(s) shall have a provision for locking to prevent unauthorized opening.

Grating:  Panels shall be aluminum with a powder coat paint finish and designed to meet OSHA OSHA 29 CFR 1926.502(c) requirements for fall protection.

Hold open feature:  A Type 316 stainless hold open device shall be provided to lock the cover in the fully open 90 degree position.

Hardware:  All hardware shall be Type 316 stainless steel.

EXECUTION

EXAMINATION

Examine substrates and openings for compliance with requirements for installation tolerances and other conditions affecting performance.  Proceed with installation only after unsatisfactory conditions have been corrected.

INSTALLATION

Install products in strict accordance with manufacturer’s instructions and approved submittals.  Locate units level, plumb, and in proper alignment with adjacent work.

Test units for proper function and adjust until proper operation is achieved.

Repair finishes damaged during installation.

Restore finishes so no evidence remains of corrective work.

ADJUSTING AND CLEANING

Clean exposed surfaces using methods acceptable to the manufacturer which will not damage finish.

END OF SECTION