BILCO Type SM provides a cost-effective solution for access to underground vaults that do not require the use of a flush-mounted door. The door features a concealed internal mounting flange that makes installation easy and secure. The gasketed, over-lapping cover design makes the door ideal for applications where the infiltration of contaminants is a concern.  For more information, please visit our website www.bilco.com or call 1-800-366-6530.

SECTION 083100

FLOOR ACCESS DOORS

(BILCO TYPE SM)

GENERAL

SUMMARY

Work Included:  Provide factory-fabricated floor access doors.

SUBMITTALS

Product Data:  Submit manufacturer’s product data.

Shop Drawings: Submit shop drawings including profiles, accessories, location, adjacent construction interface, and dimensions.

Warranty:  Submit executed copy of manufacturer’s standard warranty.

QUALITY ASSURANCE

Manufacturer:  A minimum of 5 years experience manufacturing similar products.

Installer:  A minimum of 2 years experience installing similar products.

Manufacturer’s Quality System: Registered to ISO 9001 Quality Standards including in-house engineering for product design activities.

DELIVERY, STORAGE AND HANDLING

Deliver products in manufacturer’s original packaging.  Store materials in a dry, protected, well-vented area. Inspect product upon receipt and report damaged material immediately to delivering carrier and note such damage on the carrier’s freight bill of lading.

WARRANTY

Manufacturer’s Warranty:  Provide manufacturer’s standard warranty.  Materials shall be free of defects in material and workmanship for a period of five years from the date of purchase. Should a part fail to function in normal use within this period, manufacturer shall furnish a new part at no charge.

PRODUCTS

MANUFACTURER

Basis-of-Design Manufacturer:  Type SM Surface Mount with Angle Frame Floor Access Door by The BILCO Company, P.O. Box 1203, New Haven, CT 06505, 1-800-366-6530, Fax: 1-203-535-1582, Web: www.bilco.com.

ACCESS DOOR

Furnish and install where indicated on plans vault access door Type SM, size [insert: width (_____) x length (_____)]. Length denotes hinge side. The floor access door shall be single leaf and pre-assembled from the manufacturer.

Performance characteristics:

Cover: Shall be reinforced to support a minimum live load of 105 psf (513kg/m2).

Operation of the cover shall be smooth and easy with controlled operation throughout the entire arc of opening and closing.

Operation of the cover shall not be affected by temperature.

Entire door, including all hardware components, shall be highly corrosion resistant.  Please consult the manufacturer when doors are to be installed in unusually harsh environments or extremely corrosive conditions.

Cover: Shall be 1/8” (3mm) aluminum diamond pattern.

Frame: Shall be ¼” x 3” x 3” (6mm x 76mm x 76mm) angle frame with internal mounting flange and 7/16” (11mm) diameter anchor holes.

Gasket:  A heavy extruded EPDM rubber gasket shall be permanently adhered to the cover.

Hinges:  Shall be heavy duty Type 316 stainless steel pintle hinges with 3/8” (10mm) Type 316 stainless steel hinge pins.

Lifting Assistance:  Manufacturer shall provide a gas strut lifting mechanism with a powder-coat finish to provide smooth, easy, and controlled cover operation throughout the entire arc of opening and to act as a check in retarding downward motion of the cover when closing.

A removable exterior turn/lift handle with a spring loaded ball detent shall be provided to open the cover and the latch release shall be protected by a flush, gasketed, removable screw plug.

Hardware:

Cover shall be equipped with an aluminum hold open arm that automatically locks the cover in the open position

A Type 316 stainless steel snap lock with fixed handle shall be mounted on the underside of the cover.

Hardware: Gas strut has a powder coat finish. All other hardware is type 316 stainless steel unless otherwise specified.

Finishes: Factory finish shall be mill finish aluminum.

EXECUTION

EXAMINATION

Examine substrates and openings for compliance with requirements for installation tolerances and other conditions affecting performance. Proceed with installation only after unsatisfactory conditions have been corrected.

INSTALLATION

Install products in strict accordance with manufacturer’s instructions and approved submittals.  Locate units level, plumb, and in proper alignment with adjacent work.

Test units for proper function and adjust until proper operation is achieved.

Repair finishes damaged during installation.

Restore finishes so no evidence remains of corrective work.

ADJUSTING AND CLEANING

Clean exposed surfaces using methods acceptable to the manufacturer which will not damage finish.

END OF SECTION